## Slide 1: Unit 7 Loop Optimization and Pipelining
ECE-GY 6463: Advanced Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
Manually pipeline simple sequential modules in System Verilog
Measure initiation interval, latency, and total latency
Control auto-pipelining in Vitis HLS
Extract resource and pipelining data from Vitis HLS synthesis reports
Unroll loops in Vitis HLS
Mitigate memory bottlenecks in unrolled loops with:
  Increased memory bit width
  Memory partitioning

## Slide 3: Outline
Pipelining in SystemVerilog
Loop Pipelining in Vitis HLS
Loop Unrolling and Memory Constraints

## Slide 4: Quadratic Example
Consider a quadratic function: (from previous unit)
For simplicity, assume are fixed parameters
Single cycle implementation to the right
Marked multiplier units

## Slide 5: Finding the Critical Path
Consider implementation with times in table
Find critical path
  Not including clk-Q and setup time
Two paths:
Path 1: x, x_reg, xsq_w2, y
  2 mults, 2 adders = 8.5 ns
Path 2: x, x_reg, x_w1, y
  1 register, 1 mult, 2 adders = 5.5 ns
Path 1 is critical
Hardware block | Value
Multiplier | = 3 ns
Adder | 1 ns
Path 1 | 3+3+1+1 = 8
Path 2 | 3+1+1=5
Hardware block | Value
Multiplier | 
Adder | 
Path 1 | 3+3+1+1 = 8
Path 2 | 3+1+1=5

## Slide 6: Timing Diagram
Timing diagram with ns (100 MHz)

## Slide 7: Multiplier Utilization
When are the multipliers busy?
Consider multiplier :
  Input is xreg available 0.5 ns after clock edge
  Max PD for multiplier is ns
  So is busy for [0.5, 3.5] ns in each interval
Rest of the time, is idle
  Not being used. “Waiting” for next input
Fraction utilization:

## Slide 8: Plotting the Utilization
Each multiplier busy only once in clock period
busy
busy

## Slide 9: Best Utilization with Single Cycle Design
From previous slide:
  Critical path delay
  Two multipliers + two adders
To close timing, assume parameters to right:
  Find min clock period
Each multipier is busy per clock period
Best utilization
Item | Value
Register (clk-Q) delay | = 0.5 ns
Multiplier PD | = 3 ns
Adder PD | 1 ns
Min set up time | 1 ns
Crtitcal path delay (in combinational logic) | 3+3+1+1 = 8
Min | 8.5+0.5+1= 9.5 ns
Item | Value
Register (clk-Q) delay | 
Multiplier PD | 
Adder PD | 
Min set up time | 
Crtitcal path delay (in combinational logic) | 

## Slide 10: A Two Cycle Design
We can improve throughput by breaking computation over two cycles
Register two intermediate terms:
  xsq = xreg * xreg
  lin_term = w1*xreg + w0

## Slide 11: Three Stages
Design is processed in three stages = 2 cycles
Stage 0
  Register input to xreg
Stage 1: Compute and register:
  xsq = xreg * xreg
  lin_term = w1*xreg + w0
Stage 2: Compute output
  y = w2*xsq + lin_term

## Slide 12: Pipelining Timing Diagram
Processing via a “pipeline”
Multipliers working simultaneously

## Slide 13: Comparison
 |  | Single Cycle Design | Two Cycle Design
Register + Setup time |  | 1.5 | 
Multiplier PD |  | 3 | 
Add PD |  | 1 | 
Critical path PD |  | 3+3+1+1=8 | 3+1=4
Min clock period |  | 9.5 | 5.5
Max throughput |  | 105 MHz | 181 MHz
Latency |  | 9.5 | 11
Multiplier utilization |  | 0.31 | 0.54
 |  | Single Cycle Design | Two Cycle Design
Register + Setup time |  | 1.5 | 
Multiplier PD |  | 3 | 
Add PD |  | 1 | 
Critical path PD |  | 3+3+1+1=8 | 3+1=4
Min clock period |  | 9.5 | 5.5
Max throughput |  | 105 MHz | 181 MHz
Latency |  |  | 
Multiplier utilization |  | 0.31 | 0.54
Pipelining: Higher throughput via better utilization

## Slide 14: General Pipelining for a Series
Insert registers on each stage
Use suffixes s0, s1, s2 to indicate stage

## Slide 15: Cycle-by-Cycle Timing
Cycle |  |  | z1_s1 | z2_s2 | y
0 | A | ? | ? | ? | ?
1 | B | A | ? | ? | ?
2 | C | B |  | ? | ?
3 | D | C |  |  | 
 |  | D |  |  | 
Cycle |  |  | z1_s1 | z2_s2 | y
0 | A | ? | ? | ? | ?
1 | B | A | ? | ? | ?
2 | C | B |  | ? | ?
3 | D | C |  |  | 
 |  | D |  |  | 

## Slide 16: Timing Terminology
Initiation Interval (II)
  Minimum number cycles between the start of two inputs entering the pipeline
Latency ()
  Number of cycles between an input and when output is available
  If input is available before end of cycle output available before end of cycle
  Equal to number of stages between registered inputs
Number of samples ()
  Number of consecutive input samples
Total processing time:

## Slide 17: Timing Terminology Visualized
Cycle |  |  | z1_s1 | z2_s2 | y
0 | A | ? | ? | ? | ?
1 | B | A | ? | ? | ?
2 | C | B |  | ? | ?
3 | D | C |  |  | 
 |  | D |  |  | 
Cycle |  |  | z1_s1 | z2_s2 | y
0 | A | ? | ? | ? | ?
1 | B | A | ? | ? | ?
2 | C | B |  | ? | ?
3 | D | C |  |  | 
 |  | D |  |  | 
Insert registers on each stage
Use suffixes s0, s1, s2 to indicate stage

## Slide 18: Pipelining with Multiple Paths
Now consider a more complex example with multiple paths
How do we pipeline this?

## Slide 19: Multi-Path Pipelining: Identify Stages
First, we draw the stages
  Shown in the vertical lines
Stage 0: Inputs to registers
  This stage will exist in non-pipeline code
Stage 1, 2, …
  Will end where we will put registers
  Ensure that each stage can be computed in sufficient time
Output stage is combinational
Stage 1
Stage 0
Stage 2
Combinational

## Slide 20: Multi-Path Pipelining: Register Locations
Place registers at stage crossing
Shown in blue circles
Note: Need register even when
  Signal is just a pass through
Stage 1
Stage 0
Stage 2
Combinational
Register locations

## Slide 21: Final Pipelined Diagram and Code
Stage 1
Stage 0
Stage 2

## Slide 22: Memory Accesses
Memory reads and writes:
  Generally take at least on cycle delay
  Hardware provides an address
  Memory location fetched with an address decoder
Pipelining must account for this delay
Example to the right:
  Takes elementwise product
  Load, product, and store are on separate cycles
Note the pipeline flush
  Tail of the pipeline for stages 1,

## Slide 23: Outline
Pipelining in SystemVerilog
Loop Pipelining in Vitis HLS
Loop Unrolling and Memory Constraints

## Slide 24: Why Use Vitis HLS?
Manual pipelining in System Verilog:
  Tedious
  Prone to mistakes
  Hard to optimize schedule
  Need to re-optimize on each technology
Vitis HLS C++
  Fully automated pipelining
  High-level description

## Slide 25: Polynomial Loop Example
Loop over cubic polynomial
Implemented with Horners method
  Bottom right
Each iteration involves
  One load from the array
  Three multiplications
  Three adds
  One store
We will implement in floating point FP32
  These are themselves pipelined
Would be hard to implement manually

## Slide 26: Message Passing Protocol
Similar protocol to previous unit
Processing in blocks
Coefficients sent in a header
Followed by data
Transaction ID
  Used to ensure synchronization
  Robust to dropped packets
Testbench or PS
CmdHdr: Coefficients num samples, trans ID
SampDatIn: Values of
Perform polynomial evaluation
RespFtr: TransId
SampDataOut: Values
RespFtr: Error Code, num read
Vitis kernel

## Slide 27: Define Data Structures
Use xilinxutils package
Define data structures in python

## Slide 28: Create a Python Golden Model
Python Golden model
Simulates the same messages
Runs python polynomial evaluation

## Slide 29: Running the Golden Model
Run the Golden model
Generate:
  Inputs
  Expected outputs

## Slide 30: Auto-Generate the Header Files
For each class, we generate a header file
Header files include:
  Fields in the data structure
  Methods for serializing and deserializing

## Slide 31: Vitis Kernel Implementation
Use array:
  Load to array, compute, write array to stream
  Computationally, adds an extra step
  But allows easy loop optimization analysis
Main loop is very simple
Note pragma HLS PIPELINE II=1
  Indicates to Vitis to try to pipeline this loop
  Try to find a schedule with II=1

## Slide 32: Running Vitis CS
Run C-simulation
  Performs functional validation
Run C-synthesis
  Performs pipelining
  Mapping of functions to resources
File to right: TCL script

## Slide 33: Parsing the Results
Vitis loop optimization results stored in XML file
Can parse results in xilinxutils CsynthParser
Allows easy automation

## Slide 34: Pipelining Results
Main processing loop
  Obtains II=1
  High latency L=30
  Needed for many FP32 multiplies

## Slide 35: Loop Carry Dependency
Not all loops can be pipelined
Consider merge sort
  Given two sorted lists
  Find a merged sorted list
Algorithm:
  C code to the right
  Compare current and
  Places smaller one on list
  Increments counter for the selected element

## Slide 36: Merge Sort Example
1 | 2
4 | 3
10 | 6
1 | 2
4 | 3
10 | 6
0 | 0 | 0 | 1 | 2 | 1
1 | 1 | 0 | 4 | 2 | 2
2 | 1 | 1 | 4 | 3 | 3
3 | 1 | 2 | 4 | 6 | 4
4 | 2 | 2 | 10 | 6 | 6
5 | 2 | 3 | 10 | X | 10
0 | 0 | 0 | 1 | 2 | 1
1 | 1 | 0 | 4 | 2 | 2
2 | 1 | 1 | 4 | 3 | 3
3 | 1 | 2 | 4 | 6 | 4
4 | 2 | 2 | 10 | 6 | 6
5 | 2 | 3 | 10 | X | 10

## Slide 37: Pipelining Limit
Consider main loop body needed to the right
Stage 0 of iteration
  Depends on stage 1 completion in iteration
  Why? Since addresses and are updated
Implication: Each iteration will need:
  Stage 0 iteration
  Stage 1 iteration
  Stage 0 iteration
Minimum II=2
Called a loop carry dependency

## Slide 38: Outline
Pipelining in SystemVerilog
Loop Pipelining in Vitis HLS
Loop Unrolling and Memory Constraints

## Slide 39: Loop Unrolling
Simple idea: Repeat processing in each cycle
Unroll by 2
  Need half the number of iterations
  But double the logic

## Slide 40: Loop Unrolling in Vitis
Can be done with a simple pragma
No need to manually unroll!
Handles cases when is not divisible by unroll factor
=

## Slide 41: Memory Bottleneck
Memory bottleneck
  Loop unrolling is often limited by memory accesses
Consider vector multiply SV code
Stage 0 needs:
  Two reads from and two reads from
Stage 2 needs:
  Two writes to

## Slide 42: Single Port Memory
Recall memory architecture from Unit 4
Basic memories are single port
There is a single address decoder
Can read / write one word in a cycle
Address input bits
Address decoder Selects one of
wordlines
wordlines
Data Bus
data words
R/W

## Slide 43: Three Solutions
Solution 1: Use a true multi-port RAM
  Most general. Allows read and write from any combination of addresses
  Xilinx FGPA BRAMs are two port
  But most costly in hardware
Solution 2: Use a wider bitwidth
  Say 64 bits to read two 32 bit numbers
  Works only when the accesses are contiguous
Solution 3: Bank or partition memory
  Divide memory into partitions
  Each partition has its own decoder
  Works if accesses can be across different partitions

## Slide 44: Mutli-Port RAMs
Allow arbitrary read / writes
  Except for read-write collisions to same address in same cycle
BRAM in FPGAs generally only support true two port
BMutli-port SRAMs in ASICs are expensive
Memory
Address Decoder 2
Data1, Addr1
Address Decoder 1
Data2, Addr2

## Slide 45: Using Wider Bit widths
Wide bit width design
Only one R/W to each array
Can pipeline with II=1
But need accesses to be contiguous
Narrow bit width design
Access only one word per cycle
Memory bottleneck