## Slide 1: Unit 3 Floating and Fixed Point Numbers
ECE-GY 6463: Advanced Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Today’s Lecture
How do we represent numeric values in a finite numbers of bits?
More generally, how can values be compressed?
What representations are computationally simple?
What representations result in good computational approximations?
The world is continuous and infinite, but computers are finite

## Slide 3: Example 1: Embedded LLMs
Full LLMs require massive amounts of memory
  Cannot work on embedded devices
Quantization
  Aggressive reduction in number of bits / parameter
  Ex: INT4 vs. FP32
New techniques have enabled very low footprint
  Often 1 to 1.5 GB
  Fits on commercial smartphones
Performance often remains excellent
  With judicious choice of approximation techniques
Kurtic, Eldar, et al. "“Give Me BF16 or Give Me Death”? Accuracy-Performance Trade-Offs in LLM Quantization." Proceedings of the 63rd Annual Meeting of the Association for Computational Linguistics (Volume 1: Long Papers). 2025.

## Slide 4: Example 2: Next-Generation Wireless
Massive MIMO systems in cellular base stations
  100s – 1000s of antennas
  Each antenna gets data at ~1 Gsamp/s
Data rate and processing is overwhelming
Very low-rate quantization has been key
  2- 4 bits per antenna
Uplink performance vs number of quantization levels
Jacobsson, S., Durisi, G., Coldrey, M., Gustavsson, U., & Studer, C. (2017). Throughput analysis of massive MIMO uplink with low-resolution ADCs. IEEE Transactions on Wireless Communications, 16(6), 4038-4051.

## Slide 5: Compression Research at NYU
ML techniques at the forefront for learning new compression
NYU has several leading researchers in the area
Ballé, J., Laparra, V., & Simoncelli, E. P. (2016). End-to-end optimized image compression. arXiv preprint arXiv:1611.01704.
Jona Balle, NYU

## Slide 6: Learning Objectives
Represent numbers in floating point and fixed point
Implement arithmetic operations efficiently in these formats
Identify cases for overflow
Evaluate approximation errors via simulation
Optimally select scaling factors and parameters for the formats
Convert floating point algorithms to fixed point

## Slide 7: Outline
Floating Point Numbers
Fixed Point Numbers
Optimal Scaling of Fix Point Numbers
Converting Floating Point Algorithms to Fixed Point

## Slide 8: Limitations of Integers
Unit 1 introduced two numeric types:
  = signed bit integers
  = unsigned bit integers
Problem 1. Cannot handle fractional components
  Ex: 7.9, -12.2
  Rounding may cause excessive approximation error
Problem 2. Limited range
  Values overflow for and for

## Slide 9: Simple Floating Point
Fixed point
Signed bit:
  1, One bit
Exponent, bits
Mantissa, significand, bits
  Unsigned integer. Not two complement
  is the precision
Fixed scale factor
  Constant, no bits
  Used to set range of
  More later
1
Bits=
bits total

## Slide 10: Example
Consider some values with:
  Precision Exponent width =
  Scale
  These values are never used. Just for demo
Total number of bits = bits
Mantissa range is Exponent range
Table to the right shows values with

## Slide 11: Example Problem

## Slide 12: Solution

## Slide 13: Terminology
To compare ways of representing numbers, we introduce some terminology
Class or Format: A finite set of real-valued numbers
  Example:
Bit representation: The bit encoding used to store each element in the class:
  For integer: Representation is the two-complement or unsigned integer
  For FP: representation is the triple
Decoded or numeric value: The real-value for a given bit representation
  Example:

## Slide 14: Dynamic Range
A benefit of Floating point is its dynamic range
Dynamic range: Given a number class:
  Represents span between the max before overflow and underflow
Often quoted in dB:
Or bits:

## Slide 15: Dynamic Range of Integers
Consider signed bit integers:
Max value:
Min non-zero value:
Hence dynamic range of integers:
For integers, dynamic range is:
  equal to number of non-sign bits

## Slide 16: Floating-Point Dynamic Range
Recall:
Largest value for :
Smallest non-zero value for
Dynamic range:
For floating point:
  Grows exponentially with

## Slide 17: Example Comparison
32-bit integer:
  Range goes from 1 to
  Dynamic range in linear scale
  bits
32-bit floating point:
  Dynamic range in bits: bits
  Dynamic range in linear scale
FP has orders of magnitude more range

## Slide 18: IEEE-754 Floating Point Standard
Format | Mantissa bits (stored) | Significand precision (with implicit 1) | Exponent bits
FP16 (half) | 10 | 11 | 5
FP32 (single) | 23 | 24 | 8
FP64 (double) | 52 | 53 | 11

## Slide 19: IEEE 754 Normal and Sub-Normal
For FP32: precision and exponent width
Uses a two regions
Normal region:
  Exponent in range
  In this region:
  The is as if the has an implicit leading bit of
  Note that
Sub-normal region:
  Exponent
  In this region:
  Used for small numbers

## Slide 20: IEEE 754 Properties
Single precision (FP32):
  Largest normal
  Smallest normal
  Smallest sub-normal
  Vastly greater range than 32-bit integers
Double precision (FP64):
  Largest normal
  Smallest normal
  Smallest sub-normal

## Slide 21: Floating Point Addition
Consider two numbers in normal region (sub-normal performed similarly)
We need the representation for the sum:
WLOG: Assume For simplicity assume: (other cases are similar)
Then:
Value
Since we need for normal numbers, we shift
If set otherwise
Take

## Slide 22: Resulting Algorithm
Given two numbers: with
Compute
If set
Else
Set
Handle overflow and underflow
Then:
Conclusion: We can perform addition of two FP numbers
But requires considerable extra logic for multiple cases and overflow / underflow

## Slide 23: Floating Point Multiplication
Consider two numbers in normal region (sub-normal performed similarly)
We need the representation for the product:
WLOG: Assume
Then: where (XOR) and
We need If :
  and
Handle overflow and underflow
Can perform multiplication, but requires considerable extra control logic

## Slide 24: Comparison
Integer 32 32-bit multiplier
  Implementation requires just the product: 64-bit result
FP32 FP32 multiplier
  Significand multiply: 24×24 → 48‑bit product (including hidden bit).
  Exponent path: add exponents, subtract bias, detect overflow/underflow.
  Normalization: possible shift + exponent adjust.
  Rounding: guard/round/sticky bits, increment logic, possible renormalization.
  Special cases: zeros, subnormals, infinities, NaNs, sign rules.
FP multiplication typically takes 2 to 4 complexity

## Slide 25: Outline
Floating Point Numbers
Fixed Point Numbers
Optimal Scaling of FixP Numbers
Converting Floating Point Algorithms to Fixed Point

## Slide 26: Motivating In-Class Exercise
Try the following jupyter notebook

## Slide 27: Integers vs. Floating Point
Integers:
  Pro: Easy arithmetic. No extra bits for exponent
  Cons: Do not natively handle fractional components.
  Cons: Limited dynamic range
Floating point:
  Pro: Large dynamic range, handles fractional components
  Cons: Arithmetic is harder, some loss of precision to store exponent
Is there a way to handle fractions without increased computation overhead?

## Slide 28: Fixed Point
Floating point: use a mantissa and exponent:
  Both mantissa and exponent are variables
  Gives large dynamic range, but makes arithmetic more complex
Fixed point: Key idea: Fix the exponent
  is a standard integer with bits
  Scale factor is fixed, not variable. Does not need to be stored or manipulated
  Allows fractional values.

## Slide 29: Fixed Point Q Notation
and : Standard fixed-point representation
  : total number of bits
  : number of fractional bits
  = signed values, : unsigned values
Each element is simply a bit signed or unsigned integer,
  is called the integer representation
Corresponds to a real-valued number:

## Slide 30: Examples
Take
Find closest approximation with:
  and varies
Table shows:
  value (qbits): integer representation
  Floating point value:
We see as increases:
  More accurate representation

## Slide 31: Properties
Signed values: If
  There are integer bits (including one sign bit)
  Range is
Unsigned values: If
  There are integer bits
  Range is
Resolution: Minimum positive number:
Dynamic range:
  : bits
  : bits

## Slide 32: Addition and Type Casting Operations
Addition:
  Suppose that and are bit representations of and
  Sum is: with
  Addition of numeric values = Addition of the integer representations
Changing format:
  Let is the representation of
  Suppose we wish to find the representation in
  If then: Right shift and take bits
  If then: Right shift and take bits

## Slide 33: Multiplication
Multiplication with same format
  Suppose that and are bit representations of and
  with
  Multiplication of the numerical values = multiplication of integer values with
Multiplication without overflow
  To avoid overflow, make product width
Multiplication with different formats
  If and are and representations of and
  Product is is a representation of with:
  Can downshift this result

## Slide 34: Summary
 | Numeric operation | Input formats | Equivalent fixed point operation | Output format to avoid overflow
Addition with same format |  |  |  | 
Multiplication with same output precision |  |  |  | 
Multiplication with increased precision |  |  |  | 
Reduce precision | with lower precision |  |  | 
Increase precision | with higher precision |  |  | 
 | Numeric operation | Input formats | Equivalent fixed point operation | Output format to avoid overflow
Addition with same format |  |  |  | 
Multiplication with same output precision |  |  |  | 
Multiplication with increased precision |  |  |  | 
Reduce precision |  |  |  | 
Increase precision |  |  |  | 

## Slide 35: Example Problem

## Slide 36: Solution

## Slide 37: Comparison
Property | 32-bit integer | 32-bit floating point FP32 | 
Complexity | Easy | Moderately hard | Easy
Can handle fractional values | No | Yes | Yes
Dynamic range | Low | High | Low
Property |  | 32-bit floating point FP32 | 
Complexity | Easy | Moderately hard | Easy
Can handle fractional values | No | Yes | Yes
Dynamic range | Low | High | Low

## Slide 38: Outline
Floating Point Numbers
Fixed Point Numbers
Optimal Scaling of FixP Numbers
Converting Floating Point Algorithms to Fixed Point

## Slide 39: Selecting the Precision
Suppose we have a real-valued number
Want to represent as in
How do we select and ?
Total width determined by storage and complexity
How do we select ?

## Slide 40: Probabilistic Analysis
Let variable to quantize
Model as a random variable
  The HW will see different values over time
Example to right:
  Blue = PDF of
  Fixed = total bitwidth
  Red lines = Qunatization bins for
Selecting
  Tradeoff of overflow and precision
Minimal overflow Low precision
High overflow High precision
More integer bits
More fractional bits

## Slide 41: Encoding, Representation, and Decoding
Analyze any number class with three components: Encode, representation, decoding
For fixed-point, we use the notation:
  : Encodes a real number to an integer representation
  : Decodes an integer representation back to a real number
Real value
Decode
Encode
Quantized
Real value
Representation
Ex:

## Slide 42: Mean Squared Error
Consider some encoding and decoding:
  and
Suppose that real value can be modeled probabilistically
  Has a probability density function
Then we can measure the mean squared error:
  Measures the average error
  Includes error to both precision and overflow
We can then select to minimize MSE
Assumes we have a PDF of
  That is, we know what values we are expecting

## Slide 43: Optimal Selection of
Example to the left:
For each we try different
Initially MSE decreases with
  Higher precision
But then MSE increases
  Overflow
Optimal value is a few bits below

## Slide 44: Outline
Floating Point Numbers
Fixed Point Numbers
Optimal Scaling of FixP Numbers
Converting Floating Point Algorithms to Fixed Point

## Slide 45: Example: Piecewise Function
See Jupyter notebook
Consider piecewise linear function:
How do we convert this to floating point

## Slide 46: Python Model
Create a python model
Function has
  Width and fractional bits
Inputs are integer representations
Variable stored as np.int64
  Enables simply python processing
  But actual numbers will only use smaller number of bits

## Slide 47: Python Implementation
Direct operations using FP rules
Can truncate or saturate

## Slide 48: Quantization Examples
For fractional bits
  Model roughly matches
  But can see quantization error
With bits
  Values begin to overflow
  Saturation implementation clips
  Truncate gives wrap-around values

## Slide 49: Optimizing the MSE
Initially increase :
  Increases precision
  Lower MSE
But eventually
  Reduces number of integer bits
  Begins to overflow
  Fast increase in error

## Slide 50: System Verilog Module Declaration
Define width parameters
Integer inputs
Optional saturation logic

## Slide 51: Implementation
Register inputs (not shown)
Compute and in high precision
Optionally saturate
Final max