## Slide 1: Unit 6 Timing and Critical Path Analysis
ECE-GY 6463: Advanced Hardware Design
Profs. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
Skill | You will be able to
Reason about signal stability | Find when a signal is unknown after its input changes, and its stable values before and after
Compute propagation delay | Find when each signal settles: delays in series add, parallel paths wait for the latest, and a mux waits for every input
Perform static timing analysis | Find the critical path between registers and the maximum clock frequency, with clock-to-Q and setup time
Read and draw timing diagrams | Draw detailed and cycle-accurate diagrams, and describe a waveform by its value-change points
Decompose a function across clock cycles | Split a datapath into registered stages, and trade latency for clock rate
Each skill is assessed by problems in the LLM grader. The demos add what no problem tests yet: extracting a VCD file from a Vitis simulation and plotting it in Python.

## Slide 3: Outline
Static Timing Analysis in Combinational Logic
Static Timing Analysis in Sequential Logic
Sequential Logic Timing Diagrams
VCD Files and Timing Diagrams

## Slide 4: Static Timing Analysis
Timing analysis: how long signals take to pass through a circuit
Drawn as a timing diagram
It sets the clock speed, the latency and the throughput
Static timing analysis (STA)
Uses each block's maximum propagation delay
Holds for every input: not data dependent
Conservative, but a hard guarantee: the default in industry

## Slide 5: Implementing a Signal Physically
To understand timing, look at how a signal is carried physically
A binary signal has two logical values: 0 and 1
Physically, it is usually a voltage on a wire
The voltage takes continuous values
The logical value is read by thresholding it

## Slide 6: Undefined Logic Value: X or ?
Signals take time to change: they are outputs of physical circuits
In between, the value is undefined
Also called unknown or indeterminate
Written X, or ? to avoid confusion with a variable named x
So a logic signal has three values: 0, 1 and X
A fourth, Z (high impedance), comes later

## Slide 7: Undefined Regions Illustrated
Analog signal: a continuous voltage, with finite transitions
Digital signal: 0 below 20%, 1 above 80%, X in between
X is drawn grey in every timing diagram in this unit

## Slide 8: Stable Values and Propagation Delay
Stable value: the value once a transition settles
y = x2, with x changing from 4 to 5: y settles at 25
Propagation delay: the time the output takes to settle
It has two parts
Logic delay: the gates settling
Routing delay: the signal crossing the wires
Both depend on capacitance and drive current

## Slide 9: Maximum Propagation Delay
Actual delays vary: wire length, temperature, the device
Timing diagrams use the maximum propagation delay
X marks where the value is not guaranteed
Often stable well before the maximum
The maximum is conservative
Real delays may be far below it
Exceeding it is usually catastrophic

## Slide 10: Propagation Delay
PRACTICE
A signal x is unknown before 10 ns. It is 0 from 10 ns, 4 from 20 ns and 2 from 30 ns.
It passes through a circuit whose stable output is y = 2x + 1, with a propagation delay of 3 ns.
(a) List the times at which y changes and the value it takes at each. Mark the periods where y is unknown, y = ?.
(b) Draw the timing diagram of x and y from 0 to 40 ns: the unknown periods, the transition times and the values.
The input
Time [ns] | 10 | 20 | 30
x | 0 | 4 | 2
Drawing the diagram
By hand, or with waveflow's TimingDiagram: see the slide Drawing Timing Diagrams in Python, where the value "x" draws an unknown period.
Also in the LLM grader: Unit 6 › Propagation delay

## Slide 11: Propagation Delay
SOLUTION
(a) After each change of x, y is unknown for 3 ns, then settles to 2x + 1: 1, 9 and 5
Time [ns] | 10 | 13 | 20 | 23 | 30 | 33
y | ? | 1 | ? | 9 | ? | 5
Common error
Listing only (13, 1), (23, 9), (33, 5): the unknown periods are part of the answer.
(b) The timing diagram: y goes unknown the moment x changes, and settles 3 ns later
Also in the LLM grader: Unit 6 › Propagation delay

## Slide 12: Timing in a Series Circuit: ReLU + Linear
As an example, consider a more complicated circuit:
  Linear function + ReLU from Unit 2
  Used widely in machine learning
Output port
Input ports

## Slide 13: Timing Diagram for Series Connections
Linear + ReLU is a series connection: three operations, one after another
Assume the maximum propagation delays in the table
What does the timing diagram look like when the inputs change?
Hardware block | Max prop delay
Multiplier | Tmult = 3 ns
Adder | Tadd = 1.5 ns
Max operator | Tmax = 1 ns
Total | Ttot = 5.5 ns

## Slide 14: Timing Diagram of a Series
Suppose x, a and b are in transition for t ∈ [0, 2]
They are unknown, X, there
The unknown interval is written in violet
When are the downstream signals stable?

## Slide 15: Series Timing: First Block
Start with the multiplier
Its inputs are unknown in [0, 2]
Its maximum delay is 3 ns
So mult_out is unknown in [0, 5]: 3 ns longer than its inputs
Stable value: 3 × 10 = 30

## Slide 16: Series Timing: Second Block
mult_out is unknown in [0, 5]
The adder takes 1.5 ns, so add_out is unknown in [0, 6.5]
add_out goes unknown at t = 0, as soon as x does
Unknown propagates at once; stability propagates with delay

## Slide 17: Series Timing: Third Block
Like add_out: the max block takes 1 ns
y is unknown in [0, 7.5]
Total propagation delay: 5.5 ns, counted from when the inputs are stable

## Slide 18: Example Total Propagation Delay
Hardware block | Example value
Multiplier | Tmult = 3 ns
Adder | Tadd = 1.5 ns
Max operator | Tmax = 1 ns
Total | Ttot = 5.5 ns
Along a series path the delays add: Ttot = Tmult + Tadd + Tmax

## Slide 19: Example Timing Over Multiple Inputs
Each change of the inputs repeats the pattern: y is unknown until 5.5 ns after the inputs settle
Stable values: max(10·3 + 15, 0) = 45, max(−4·10 + 4, 0) = 0, max(8·12 − 5, 0) = 91

## Slide 20: Series Timing
PRACTICE
Each multiplication has a maximum propagation delay of 3 ns and the addition 2 ns. x = 0 for a long time before 10 ns, then changes to x = 4 at 10 ns and stays there. a = 3 and b = 6 are constants.
(a) What are the stable values of xsq, y and z before and after the change?
(b) Draw the timing diagram of x, xsq, y and z from 0 to 25 ns: the unknown periods (?), the transition times and the values.
SystemVerilog, combinational
xsq = x*x;
y = a*xsq;
z = y + b;
Drawing the diagram
By hand, or with waveflow's TimingDiagram: see the slide Drawing Timing Diagrams in Python, where the value "x" draws an unknown period.
Also in the LLM grader: Unit 6 › Series timing

## Slide 21: Series Timing
SOLUTION
(a) Before: xsq = 0, y = 0, z = 6
After: xsq = 16, y = 3·16 = 48, z = 48 + 6 = 54
(b) The timing diagram, right. All three go unknown at 10 ns, when x changes; x itself changes at once
xsq stable at 13 ns: 10 + 3
y stable at 16 ns: 13 + 3
z stable at 18 ns: 16 + 2
Common error
y and z go unknown at 10 ns, not when the block before them settles.
Also in the LLM grader: Unit 6 › Series timing

## Slide 22: Typical Propagation Delays: Low-End FPGA
Hardware block | FPGA resource | Typical range
32-bit adder | LUT + dedicated carry chain | 1.5–3.0 ns
16-bit multiplier | DSP48E1 block | 2.5–5.0 ns
16-bit comparator | LUT logic + carry chain | 1.0–2.0 ns
Rough delays for a low-end FPGA (e.g., Pynq Z2)
We will explain the FPGA resources more in later units
Routing delays not included
  May be large for more complex designs

## Slide 23: Typical Propagation Delays: ASIC
Hardware block | Typical structure | Typical range
32-bit adder | Kogge‑Stone / Brent‑Kung / hybrid | 150-450 ps
16-bit multiplier | Wallace/Dadda tree + final adder | 300-700 ps
16-bit comparator | XOR/AND/OR chain with early‑out | 50-300 ps
Rough delays for TSMC 16nm
Custom ASICs are much faster than FPGAs
  Easily 5 to 10x faster

## Slide 24: Timing Diagram with Multiple Paths
Now a circuit with two paths into the adder
One through xsq = x·x
One through the ReLU: r = max(x, 0)
How does the timing diagram work?
xsq = x * x;
r = (x > 0) ? x : 0;
y = xsq + r;

## Slide 25: Multi-Path Timing: Input
x changes from 0 to 4
It is in transition, unknown, for t ∈ [10, 12]

## Slide 26: Multi-Path Timing: First Steps
xsq: the multiplier takes 3 ns
Unknown in [10, 15], then 16
r: the ReLU takes 1 ns
Unknown in [10, 13], then 4
The two paths settle in parallel

## Slide 27: Multi-Path Timing: Output
y goes unknown when either input does: at 10
It settles once both are stable: xsq at 15, r at 13
The adder takes 1.5 ns: y is stable at 16.5, value 20
The latest input sets the delay

## Slide 28: Multi-Path Timing
PRACTICE
x is 0 for a long time before 0 ns, unknown from 10 ns, and 4 from 12 ns. a = 3 and b = 6. Delays: multiplication 3 ns, addition 2 ns, max 1 ns.
(a) What are the stable values of z1, z2 and y before 10 ns?
(b) What are their stable values after 12 ns, once every delay has passed?
(c) Draw the timing diagram of x, z1, z2 and y from 0 to 20 ns: the unknown periods (?), the transition times and the values.
z1 = a*x;
z2 = x+b;
y = max(z1, z2); // the larger
Time [ns] | 0 | 10 | 12
x | 0 | ? | 4
Drawing the diagram
By hand, or with waveflow's TimingDiagram: see the slide Drawing Timing Diagrams in Python, where the value "x" draws an unknown period.
Also in the LLM grader: Unit 6 › Multi-path timing

## Slide 29: Multi-Path Timing
SOLUTION
(a) z1 = 0, z2 = 6, y = max(0, 6) = 6
(b) z1 = 12, z2 = 10, y = 12
(c) The timing diagram, right. All go unknown at 10 ns; x settles at 12 ns, so:
z1 at 15 ns (12 + 3), z2 at 14 ns (12 + 2)
y at 16 ns: the later of the two, plus 1
Common error
Counting from 10 ns, when x first changes: 13, 12 and 14. The delay starts when x is stable again.
Also in the LLM grader: Unit 6 › Multi-path timing

## Slide 30: Conditional Circuits
Consider a conditional block
How is it implemented in hardware?
What is its maximum propagation delay?
// mux delay = 1
if (x > 0) begin // delay = 0.5
z = func1(x); // delay = 4
end else begin
z = func2(x); // delay = 2
end
y = func3(z); // delay = 1.5

## Slide 31: Conditionals as Multiplexers
Multiplexer: passes one of its inputs, chosen by a condition
The inputs and the condition are all computed in parallel
Each needs its own hardware
The branch not taken saves nothing
The output settles after the slowest input, plus the mux delay

## Slide 32: Propagation Delay with a Multiplexer
Arrival times in violet
The slowest mux input is z = f1(x): 4 ns
Not the branch x happens to select: STA covers every input
The mux adds 1 ns: z is stable at 5 ns
y is stable 1.5 ns later: 6.5 ns
Homework in the LLM grader: Unit 6 › Timing with multiplexer

## Slide 33: Critical Path
Critical path: the path with the largest propagation delay
Here: x → f1 → mux → f3 → y
To speed up the circuit, shorten the critical path
A faster f1 helps
A faster f2 does not

## Slide 34: Critical Path Example
Functions F1 … F4, with x1 = F2(F1(a)), x2 = F3(b), y = F4(x1, x2)
Path 1: F1 → F2 → F4
3 + 2 + 2.5 = 7.5 ns: the longest, so the critical path
Path 2: F3 → F4
3.5 + 2.5 = 6 ns: not critical

## Slide 35: Delay Depends on the Implementation
Example: y = a + b + c + d, with each addition taking D
Synthesis tools look for a low-delay implementation
IN SERIES: DELAY 3D
AS A TREE: DELAY 2D

## Slide 36: Outline
Static Timing Analysis in Combinational Logic
Static Timing Analysis in Sequential Logic
Sequential Logic Timing Diagrams
VCD Files and Timing Diagrams

## Slide 37: Synchronous Logic
Now: static timing analysis of synchronous logic
In this unit we assume
All registers are clocked on the same rising edge
The clock reaches every register at the same time: no clock skew
Reset paths are not analyzed
always_comb begin
x_next = f(x);
end
always_ff @(posedge clk) begin
x <= x_next;
end

## Slide 38: STA for Synchronous Logic
STA checks every register-to-register path: from a register output to a register input
Two conditions
No path arrives too late: the next value must be stable a setup time before the next rising edge
No path arrives too early: a register's input must stay stable a hold time after the edge

## Slide 39: Setup and Hold Time
Registers are usually D flip-flops
Correct operation needs D stable around the rising edge
Setup margin: from D stable to the edge
Must exceed the setup time
Hold margin: from the edge to D changing
Must exceed the hold time

## Slide 40: Clock-to-Q Time
Clock-to-Q time: from the rising edge to a stable output Q
Loosely called the register delay
The time to pass D through to Q

## Slide 41: Typical Times
Technology | Clock-to-Q | Setup | Hold | Typical clock period
Low-end FPGA (PYNQ-Z2 / Zynq-7000, Artix-7) | 300–600 ps | 150–300 ps | 0–150 ps | 5–10 ns (100–200 MHz)
High-end FPGA (UltraScale+, Stratix 10) | 150–300 ps | 100–200 ps | 0–120 ps | 1.5–3 ns (330–670 MHz)
ASIC, modern node (7–28 nm) | 20–80 ps | 20–60 ps | −20 to +40 ps | 0.3–1 ns (1–3 GHz)
Modern nodes can have a negative hold time: the input may change slightly before the edge.

## Slide 42: Register-to-Register Paths
always_comb begin
z0 = func1(x0);
z1 = func2(x1);
x_next0 = func3(z0, z1);
x_next1 = func4(z0, x1);
end
always_ff @(posedge clk) begin
x0 <= x_next0;
x1 <= x_next1;
end
Register-to-register path: from any register output to any register input
Primed values x0′, x1′ are the values in the next cycle
FOUR PATHS
x0 → f1 → f3 → x0′
x0 → f1 → f4 → x1′
x1 → f2 → f3 → x0′
x1 → f4 → x1′

## Slide 43: Verifying the Setup Time
For now, assume the hold condition is met
Every path must arrive a setup time before the next edge
A path's delay has two parts
Tclk-Q: the register that launches it
TPD: the combinational logic
Tcrit: the largest TPD, along the critical path
To meet timing: Tclk ≥ Tcrit + Tclk-Q + Tsetup

## Slide 44: Meeting or Failing Timing
Tclk ≥ Tcrit + Tclk-Q + Tsetup
Tclk: the clock period; fclk = 1 / Tclk, the clock frequency
Tcrit: the delay of the critical path through the combinational logic
Tsetup: the minimum setup time; Tclk-Q: the clock-to-Q time
If it holds, the design meets timing
Otherwise it fails timing: a timing violation

## Slide 45: Example: Finding the Critical Path
Component | Value [ns]
f1 PD | 1.8
f2 PD | 2.2
f3 PD | 2.3
f4 PD | 2.1
Tclk-Q | 0.2
Tsetup | 0.1
Arrival times computed block by block, as for combinational logic
x_next0: max(1.8, 2.2) + 2.3 = 4.5; x_next1: 1.8 + 2.1 = 3.9
Critical path x1 → f2 → f3 → x0′: Tcrit = 4.5 ns

## Slide 46: Example: Maximum Clock Frequency
From the previous slide, Tcrit = 4.5 ns
So to meet timing
Tclk ≥ Tcrit + Tclk-Q + Tsetup
= 4.5 + 0.2 + 0.1 = 4.8 ns
Maximum clock frequency
fclk = 1 / Tclk ≤ 1 / 4.8 ns ≈ 208 MHz
Homework in the LLM grader: Unit 6 › Critical path

## Slide 47: Meeting the Minimum Hold Time
Consider a simple delay line
A naive implementation has a very short path from x0 to the input of x1
It could violate the minimum hold time
Place and route fixes this: it inserts delay where a path is too short
So in a reasonable synchronous design, the RTL need not worry about hold time
always_ff @(posedge clk) begin
x0 <= x;
x1 <= x0;
end

## Slide 48: Outline
Static Timing Analysis in Combinational Logic
Static Timing Analysis in Sequential Logic
Sequential Logic Timing Diagrams
VCD Files and Timing Diagrams

## Slide 49: Synchronous Logic in Detail
A counter: f(x) = x + 1
Every synchronous circuit has two delays
Clock-to-Q: edge → register output; 2 ns here
Combinational PD: register output → next value; 3 ns here

## Slide 50: Detailed Timing Diagram
A diagram with every delay is a detailed timing diagram
Sometimes called the real timing diagram
It shows register delays and every propagation delay
Good for reasoning about precise timing: clock speed, throughput, …
But too much detail to see what the circuit does

## Slide 51: Cycle-Accurate Timing Diagram
Abstract or cycle-accurate timing diagram
Every delay → 0
No unknown (X) regions
Simpler to see what the circuit does
Each cycle shows the value just before the rising edge that ends it

## Slide 52: ReLU + Linear: Synchronous Module
Now the synchronous version of ReLU + linear, as in Unit 2
Two ports are added
clk: the clock
rst_n: an active-low reset
module relu_lin (
input logic clk,
input logic rst_n,
input int x,
input int a,
input int b,
output int y
);

## Slide 53: Synchronous Implementation
The same implementation as in Unit 2
Next values computed in an always_comb block
int x_reg, a_reg, b_reg;
always_ff @(posedge clk or negedge rst_n) begin
if (!rst_n) begin
x_reg <= 0; a_reg <= 0; b_reg <= 0;
end else begin
x_reg <= x; a_reg <= a; b_reg <= b;
end
end
always_comb begin
int mult_out, add_out;
mult_out = x_reg * a_reg;
add_out = mult_out + b_reg;
y = (add_out > 0) ? add_out : 0;
end
endmodule

## Slide 54: STA of the Synchronous Module
Assume the delays in the table
Ignore the clock-to-Q time for now
The arrival time at each stage is in violet
Hardware block | Max prop delay
Register | 0 ns
Multiplier | Tmult = 3 ns
Adder | Tadd = 1.5 ns
Max operator | Tmax = 1 ns
Total: critical path | Tcrit = 5.5 ns

## Slide 55: ReLU + Linear Timing Diagram
Hardware block | Max prop delay
Register | 0 ns
Multiplier | Tmult = 3 ns
Adder | Tadd = 1.5 ns
Max operator | Tmax = 1 ns
Total: critical path | Tcrit = 5.5 ns
Meets timing: Tclk = 10 ns > Tcrit = 5.5 ns
y settles 5.5 ns after each rising edge, well before the next one.

## Slide 56: Maximum Clock Frequency Example
With clock-to-Q and setup time ignored, the minimum clock period is
Tclk = Tcrit = 5.5 ns
Maximum clock frequency
fclk = 1 / 5.5 ns ≈ 182 MHz
With Tclk-Q and Tsetup, it would be lower

## Slide 57: Quadratic Example
A quadratic: y = w2x2 + w1x + w0
w0, w1, w2 are fixed parameters
A single-cycle implementation, right
module quad_func #(
parameter int w2 = 0,
parameter int w1 = 0,
parameter int w0 = 0
) (
input logic clk,
input int x,
output int y
);
int x_reg;
always_ff @(posedge clk) begin
x_reg <= x;
end
always_comb begin
int xsq, xsq_w2, x_w1;
xsq = x_reg * x_reg;
xsq_w2 = w2 * xsq;
x_w1 = w1 * x_reg;
y = xsq_w2 + x_w1 + w0;
end
endmodule

## Slide 58: Finding the Critical Path
Hardware block | Example value
Register | Treg = 1 ns
Multiplier | Tmult = 4 ns
Adder | Tadd = 1.5 ns
Path 1 | 1 + 4 + 4 + 1.5 + 1.5 = 12
Path 2 | 1 + 4 + 1.5 + 1.5 = 8
Two paths from x_reg to y
Path 1, through xsq and xsq_w2: a register, 2 multiplies, 2 adds: 12 ns
Path 2, through x_w1: a register, 1 multiply, 2 adds: 8 ns
Path 1 is critical
Maximum clock frequency = 1 / 12 ns ≈ 83 MHz
So it fails timing at 100 MHz

## Slide 59: A Two-Cycle Design
Improve the clock rate by spreading the computation over two cycles
Register two intermediate terms
xsq = xreg * xreg
lin_term = w1*xreg + w0
int xreg, xsq, lin_term;
always_ff @(posedge clk) begin
xreg <= x;
xsq <= xreg * xreg;
lin_term <= w1 * xreg + w0;
end
always_comb begin
y = w2 * xsq + lin_term;
end

## Slide 60: Three Stages
The design now runs in three stages, over two cycles
Stage 0: register x into xreg
Stage 1: compute and register xsq and lin_term
xsq = xreg · xreg
lin_term = w1·xreg + w0
Stage 2: compute y = w2·xsq + lin_term

## Slide 61: Critical Path with Three Stages
Hardware block | Example value
Register | Treg = 1 ns
Multiplier | Tmult = 4 ns
Adder | Tadd = 1.5 ns
Path 1 | 1 + 4 = 5
Path 2 | 1 + 4 + 1.5 = 6.5
Path 3 | 1 + 4 + 1.5 = 6.5
Measure every path from register to register
Path 1: x_reg → the xsq register: 1 register, 1 multiply
Path 2: x_reg → the lin_term register: 1 register, 1 multiply, 1 add
Path 3: xsq, lin_term → y: 1 register, 1 multiply, 1 add
Critical path delay: 6.5 ns, down from 12
Maximum clock frequency = 1 / 6.5 ns ≈ 154 MHz
Homework in the LLM grader: Unit 6 › Two cycle datapath

## Slide 62: Two-Cycle Timing Diagram
w0, w1, w2 = 4, −7, 5
x = 10, −4, 8
y = 434, 112, 268

## Slide 63: Latency, Throughput and Pipelining
Run the design at a 100 MHz clock
Latency
An input captured at one rising edge is out before the edge two cycles later
Latency = 2 cycles = 20 ns
Throughput
A new input every cycle: 100 M inputs/s
This is a pipeline: several inputs are in progress at once

## Slide 64: Performance Comparison
 | Single-cycle design | Two-cycle design
Critical path | 12 ns | 6.5 ns
Maximum clock frequency | ≈ 83 MHz | ≈ 154 MHz
Maximum throughput | ≈ 83 M inputs/s | ≈ 154 M inputs/s
Latency | 1 cycle = 12 ns | 2 cycles = 13 ns
Pipelining: for a small increase in latency, a large gain in throughput.

## Slide 65: The Demo: Latency and the Clock
sdrangan.github.io/hwdesign — Demos › Timing and the Clock
RUN THE SWEEP
cd demos/timing/quad
python quad_build.py --list-steps
python quad_build.py --force-step sweep
WHAT TO WATCH FOR
The quadratic with no AXI: plain wires and ap_start / ap_done
Latency: 0 cycles at 50 MHz, 2 at 100 MHz, 9 at 300 MHz
In ns it does not fall: 20 ns at 100 MHz, 30 ns at 300 MHz
Fails timing at 400 MHz; pipelined, a new input every cycle

## Slide 66: Outline
Static Timing Analysis in Combinational Logic
Static Timing Analysis in Sequential Logic
Sequential Logic Timing Diagrams
VCD Files and Timing Diagrams

## Slide 67: Value-Change Points
Simulation tools trace values over time for large numbers of signals
Data on each signal is typically stored via value-change points
  Value change points also called value-change events, transitions, …
Definition: A signal has value-change points if:

## Slide 68: Drawing Value-Change Points
A timing diagram can be drawn from the value-change points
Example with two signals, times in ns
x: (3, 5), (20, 17), (40, 8)
y: (12, 3), (25, 12), (35, 0)
Before its first point, a signal is unknown

## Slide 69: VCD Files from a Vitis Simulation
Co-simulation records waveforms in a .wdb file
An AMD format that only the Vivado viewer opens
A VCD (value change dump) is an open text format
A header naming the signals, then the time of every change
The demo builds re-run the RTL simulation with VCD logging on: the extract_vcd step
Port signals by default; --trace-level all for every internal one
THE EXAMPLE ON THE LAST SLIDE, AS A VCD
$timescale 1ns $end
$scope module top $end
$var wire 32 ! x [31:0] $end
$var wire 32 " y [31:0] $end
$upscope $end
$enddefinitions $end
#3
b101 !
#12
b11 "
#20
b10001 !
#25
b1100 "
...

## Slide 70: Drawing Timing Diagrams in Python
waveflow (in pysilicon) reads VCD files and draws timing diagrams; the value "x" is drawn as the grey unknown region
from waveflow.utils.timing import SigTimingInfo, TimingDiagram
xsig = SigTimingInfo("x", times=[0, 3, 20, 40],
values=["x", "5", "17", "8"])
ysig = SigTimingInfo("y", times=[0, 12, 25, 35],
values=["x", "3", "12", "0"])
td = TimingDiagram()
td.add_signals([xsig, ysig])
ax = td.plot_signals(trange=[0, 50], add_clk_grid=False)
ax.set_xlabel("time [ns]")
The figure the code draws: the example from two slides back.

## Slide 71: The Demo: Timing Diagrams from Vitis
sdrangan.github.io/hwdesign — Demos › AXI4-Streaming › Viewing the Timing Diagram
RUN THE WHOLE FLOW
cd demos/stream/avgfilt
python avgfilt_build.py --list-steps
python avgfilt_build.py --through extract_vcd
python avgfilt_build.py --through timing_diagram
WHAT TO WATCH FOR
extract_vcd re-runs the RTL simulation with VCD logging switched on
timing_diagram reads the VCD and decodes the stream off the wires
A sample moves on a rising edge where TVALID and TREADY are both high
The scalar-function demo does the same for an AXI4-Lite IP
Measured on the RTL: a latency of 19 cycles, then 200 samples out in 200 cycles.
The latency and throughput this unit computes by hand, read off a real waveform.